## Slide 1: Arbiter PUF Based Mutual Authentication and Session Key Agreement Scheme for IoT
Presented By
Saurabh Soni
MTech CSE
24CS4131
Guided By
Dr. Subhas Chandra Sahana
Department of Computer Science & Engineering
National Institute of Technology Durgapur

## Slide 2: Introduction
IoT devices are rapidly increasing in modern applications.
Traditional authentication relies on stored secret keys.
Stored keys are vulnerable to attacks and cloning.
Lightweight hardware-based security is required.
PUFs provide unique hardware fingerprints.

## Slide 3: Problem Statement
Issue :
Secret keys stored in memory can be extracted.
Software-based authentication is vulnerable.
Existing systems authenticate only one device.
Secure session key establishment is challenging.
Need:
A lightweight hardware-based mutual authentication framework.

## Slide 4: Literature Review
Existing Arbiter PUF systems support only single-device authentication.
Many lightweight IoT security systems lack secure communication.
Existing PUF-based methods do not support dynamic session key generation.
Research gap exists in mutual authentication and encrypted communication.

## Slide 5: Existing APUF RESULT
[2]

## Slide 6: Existing PUF-Based Authentication Schemes
Paper | Mutual Auth | Session Key | FPGA | 
LFSR-APUF (2023) | Yes | Partial | Yes | 
PUF Key-Exchange (2023) | Yes | Yes | No | 
PA-PUF (2022) | No | No | Yes | 

## Slide 7: Objectives
FPGA-based Arbiter PUF implementation
Generate CRPs
Mutual authentication
Multi-challenge verification
Session key generation
AES-based secure communication
Replay attack protection

## Slide 8: Why PUF Instead of Classical Cryptography?
Limitations of Classical Cryptography
Secret keys are permanently stored in memory
Stored keys are vulnerable to:
Physical attacks
Key extraction
Cloning
Reverse engineering
Heavy cryptographic operations increase computational overhead
Resource-constrained IoT devices have limited power and memory
Advantages of APUF-Based Security
No permanent secret key storage required
Responses generated from intrinsic hardware variations
Extremely difficult to clone or duplicate
Lightweight and low-power implementation
Dynamic session key generation improves security
Suitable for secure IoT authentication application

## Slide 9: Physical Unclonable Function
PUF acts as a hardware fingerprint.
Uses manufacturing variations.
Generates unique responses.
No permanent key storage required.
Suitable for lightweight IoT security.

## Slide 10: Arbiter PUF Architecture
Two parallel signal paths are created.
Challenge bits control multiplexers.
Arbiter detects faster path.
Top path faster → Response = 1
Bottom path faster → Response = 0
Hardware:
Basys-3 FPGA | Artix-7 | Vivado

## Slide 11: CRP Generation Workflow
Challenge Input → APUF → Response Generation → UART Transmission → CSV Database
CRPs are used for:
Authentication
Session key generation

## Slide 13: Proposed System Architecture
Components:
IoT-A
Authentication Server
IoT-B
Features:
Mutual authentication
Session key agreement
AES secure communication
Timestamp-based replay protection

## Slide 15: Mutual Authentication Scheme
m1 : IoT-A → Server
m2 : Server → IoT-A (CA)
m3 : Server → IoT-B (CB)
m4 : IoT-A → Server (RA)
m5 : IoT-B → Server (RB)
m6 : Server → IoT-A (RB)
m7 : Server → IoT-B (RA)

## Slide 16: Authentication & Session Key
7 random challenges generated
Threshold verification: Match ≥ 5/7
Session Key:
SK = SHA256(RA || RB || Timestamp)
Features:
Dynamic session key
Unique per session
No permanent key storage

## Slide 17: Replay Attack Protection
Timestamp included during authentication.
Server validates session freshness.
Expired authentication requests are rejected.
Prevents replay attacks.

## Slide 18: Secure Communication
Plain Text → AES Encryption → Socket Communication → AES Decryption
Example:
Encrypted Message:
GGSfSEIHWMvliFtXCuX8eSSHNPdvbA6MXyibDfJYTTI=
Decrypted Message:
Hello from IoT-A

## Slide 19: Experimental Results
SINGLE APUF
Uniformity : 50.23%
Reliability : 98.98%
Uniqueness : --
Observations:
High reliability
Near-ideal uniformity
Strong uniqueness
DOUBLE APUF
Uniformity : 51.40/48.60
Reliability : 92.61%
Uniqueness : 100%

## Slide 20: comparison with APUF result

## Slide 21: FPGA Resource Utilization
LUTs : 102
MUXs : 127
Slices : 26
[1]
Observations:
Lightweight implementation
Area efficient
Suitable for IoT devices

## Slide 22: Comparison Existing PUF-Based Authentication Schemes
Paper | Mutual Auth | Session key | FPGA
LFSR APUF (2023)[4] | Yes | Partial | Yes
PUF Key Exchange 2023[2] | Yes | Yes | No
PA-PUF 2022[3] | No | No | Yes
Proposed Scheme | Yes | Yes | Yes

## Slide 23: Security Analysis
Resistant to cloning attacks
Resistant to replay attacks
Resistant to key extraction
Resistant to hardware tampering
Partial risk against ML modeling attacks

## Slide 24: Proposed Work
Implemented a lightweight FPGA-based Arbiter PUF authentication system for IoT security.
Achieved mutual authentication between two IoT devices instead of only single-device authentication.
Introduced multi-challenge threshold verification to improve authentication reliability.
Generated a dynamic session key using PUF responses and SHA-256 without storing permanent secret keys.
Integrated AES-based secure communication after authentication.
Added timestamp-based replay attack protection.
Designed an area-efficient hardware architecture suitable for resource-constrained IoT devices.

## Slide 25: Conclusion & Future Work
Successfully implemented FPGA-based APUF authentication.
Achieved mutual authentication.
Generated shared session key.
Established AES secure communication.
Future Work:
XOR PUF
Wireless communication

## Slide 26: REFERENCES
[1] S. Roy, D. Das, and B. Sen, “Secure and Lightweight Authentication Protocol Using PUF for the IoT-Based Wireless Sensor Network,” ACM Journal on Emerging Technologies in Computing Systems, vol. 20, no. 1, Article 3, Nov. 2023.
[2] V. P. Yanambaka, S. P. Mohanty, E. Kougianos, and D. Puthal, “PMsec: Physical Unclonable Function-Based Robust and Lightweight Authentication in the Internet of Medical Things,” IEEE Transactions on Consumer Electronics, vol. 65, no. 3, pp. 388–397, Aug. 2019.
[3] C. Prabhunath G. and A. P. Shah, “Fredkin Gate-Based Arbiter PUF Design Through Challenge Obfuscation Using Garbage Outputs,” Integration, the VLSI Journal, vol. 106, 2026.
[4] Al-Meer, A., & Al-Kuwari, S. (2022). Physical Unclonable Functions (PUF) for IoT Devices. arXiv preprint arXiv:2205.08587.

## Slide 27: Thank You
Saurabh Soni
MTech CSE
24CS4131
NIT Durgapur